## Slide 1
Andrea Brambilla1
Øyvind Andreassen2,3
Helwig Hauser1
Integrated Multi-aspect Visualization of 3D Fluid Flows
1 University of Bergen, Norway
2 Norwegian Defence Research Establishment, Norway
3 University Graduate Center at Kjeller, Norway

## Slide 2
CFD Simulations
Brambilla et al.
Notes: Talk about flow vis
Starting point: CFD simulation
Exhaust manifold with 3 inlets and 1 outlet, only the central inlet is currently active

## Slide 3
Velocity
Brambilla et al.
Notes: Simulation produce a velocity vector fields
Instantaneous motion of fluid’s particles (infinitesimally small)
Velocity alone cannot capture the overall complexity of the flow behavior
Domain experts often resort to derived attributes for analysis

## Slide 4
Flow aspects
Brambilla et al.
Velocity (motion)
Rate of strain (deformation)
Vorticity (rotation)
Notes: All these attributes are connected
There are known relationships between them. E.g., the vorticity transport equation
It is important to look at these attributes simultaneously in order to grasp their relationships

## Slide 5
Related work
Brambilla et al.
De Leew and van Wick ‘93
Schafhitzel et al. ‘11
Helgeland et al. ‘07
Bürger et al. ‘08
Kirby et al. ‘99
Notes: Investigated alone OR multivariate visualization

## Slide 6
Integrated Multi-aspect Vis
Brambilla et al.

## Slide 7
Requirements
Brambilla et al.
Visual representation
  Convey local information
  Handle vector and tensor data
Manage visibility issues
  Focus + Context visualization
  Exploit data coherency
Glyph
  Color -> magnitude
  Geometry -> direction
Velocity magnitude
Vorticity magnitude
Rate of Strain magnitude
min max
min max
min max

## Slide 8
Multiple Focus + Context
Brambilla et al.
Different flow aspects can be more or less relevant
  Swirling motion in a constant laminar flow?
The relevance of an attribute can vary over the domain
Multiple relevance measures

## Slide 9
Relevance measures
Brambilla et al.
For each attribute a
  Define a set of potential locations Pa
  Define relevancea: Pa -> [0, 1]
ux
min max min max
1
0
relevance
uy
0
1
relevance
Relevance measures are user defined

## Slide 10
Relevance measures
Brambilla et al.
For each attribute a
  Define a set of potential locations Pa
  Define relevancea: Pa -> [0, 1]
ux
min max min max
1
0
relevance
uy
0
1
relevance
Relevance measures are user defined
Flow feature detectors can capture physical aspects
  Hunt’s Q / λ2 / Haimes and Kenwright
1
0
relevance
λ2
min max
1
0
relevance
Q
min max

## Slide 11
Coherency and Visual Redundancy
Brambilla et al.
Information can be replicated over many samples
Visualize that information only once!

## Slide 12
Coherency measures
Brambilla et al.
A coherency measure encodes the degree of redundancy of a set of data samples
For each attribute a, coherencya: P(Pa) -> R+
Specified by the user
  4 measures implemented in our system
  More measures can be easily added
  Similar overall behaviour, but small differences
test dataset 2nd moment entropy c_diffv c_dotv
Notes: No coherency measure outperformed the other ones
Example: 5 cell radius, arrow size proportional to coherency
Coherency val = 0 means  equal samples
Higher values  incoherent samples

## Slide 13
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:

## Slide 14
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa

## Slide 15
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa

## Slide 16
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
Ap

## Slide 17
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
Ap

## Slide 18
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
Ap

## Slide 19
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
Ap

## Slide 20
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
Ap
The radius of Ap is mapped to size
The relevance of p is mapped to opacity

## Slide 21
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
Pa
The radius of Ap is mapped to size
The relevance of p is mapped to opacity

## Slide 22
Visualization strategy
Brambilla et al.
Glyph placement algorithm:
for each attribute a
.. γa = coherency threshold
.. build(Pa)
.. sort(Pa, relevancea)
.. for p in Pa
.. .. Ap = sphere around p
.. .. while coherencya(Ap) < γa
.. .. .. increase radius of Ap
.. .. place a glyph in p
.. .. Pa = Pa - Ap
Pa
Repeat until all the points have been processed
Repeat for every attribute of interest

## Slide 23
Integrated Multi-aspect Vis
Brambilla et al.

## Slide 24
Integrated Multi-aspect Vis
Brambilla et al.

## Slide 25
Integrated Multi-aspect Vis
Brambilla et al.

## Slide 26
Parameter settings
Brambilla et al.
Relevance corresponds to user’s interest
Coherency threshold
  Initially set to 10% of maximal coherency value
  Can be interactively adjusted
high thresh. mid thresh. low thresh.

## Slide 27
Final remarks
Brambilla et al.
Our visualization strategy
  Presents multiple flow aspects simultaneously
  Handles visibility issues through smart placement
  Can be easily extended
Future work
  Streamlets as a new representation
  Coherency measure based on tensor invariants
  Adapt the strategy to integral curves
  Extension to time-dependent datasets

## Slide 28
Thanks for your attention!
Brambilla et al.

## Slide 29
Square Cylinder
Brambilla et al.

## Slide 30
Flow in a Box
Brambilla et al.

## Slide 31
Flow in a Box (pruned)
Brambilla et al.

## Slide 32
Andrea Brambilla1
Øyvind Andreassen2,3
Helwig Hauser1
Integrated Multi-aspect Visualization of 3D Fluid Flows
1 University of Bergen, Norway
2 Norwegian Defence Research Establishment, Norway
3 University Graduate Center at Kjeller, Norway

## Slide 33
Exhaust Manifold
Brambilla et al.

## Slide 34
Exhaust Manifold (pruned)
Brambilla et al.

## Slide 35
Thanks for your attention!
Brambilla et al.

## Slide 36
Attributes of interest
Brambilla et al.
Velocity vector field
Rate of strain tensor
Vorticity tensor
Vorticity vector
Vorticity transport equation
Notes: All these attributes are connected
There are known relationships between them. E.g., the vorticity transport equation
It is important to look at these attributes simultaneously in order to grasp their relationships

## Slide 37
Performance
Brambilla et al.
Performance
  Relevance is pre-cumputed
  Coherency computation depends on
    Dataset size and number of relevant points
    Actual data coherency
    Exhaust Manifold (133x81x31) -> 0.128 sec (2.8GHz CPU)
  Bottleneck is the geometry generation
    Exhaust Manifold -> 0.470 sec / 1.037 sec (depth sort)
    But GPU implementation feasible!

## Slide 38
Streamline-based Pruning
Brambilla et al.

## Slide 39
Streamline-based Pruning
Brambilla et al.

## Slide 40
Vorticity
Brambilla et al.
Notes: Vorticity represent the instantaneous rotation of fluid’s particles

## Slide 41
Rate of Strain
Brambilla et al.
Notes: Rate of strain represent the instantaneous deformation of an infinitesimally small fluid’s volume